## Slide 1: Technical Support (420-1N6-AB) More Detail on Binary Math
Fall 2021

## Slide 2: Outline
How to calculate 4 + (-20) in binary? [FULL SOLUTION]
How to do these problems in general
Review: how many bits do we need to represent a number?
Similar exercises [For you to complete in class. Similar problems on assignment 1 and test 1]

## Slide 3: How do we calculate 4 + (-20) in binary?
Steps
Converting 4 and 20 to binary
Apply Two’s Complement rule to (-20)
Add the two binary numbers
Check your answer: convert the result to decimal

## Slide 4: How do we calculate 4 + (-20) in binary?
Step 1. Converting 4 and 20 to binary
Steps | Outcome | Remainder
1 | 4 | 0
2 | 2 | 0
3 | 1 | 1
Stop | 0 | 
(4)10 = (100)2
Steps | Outcome | Remainder
1 | 20 | 0
2 | 10 | 0
3 | 5 | 1
4 | 3 | 0
5 | 1 | 1
Stop | 0 | 
(20)10 = (10100)2

## Slide 5: How do we calculate 4 + (-20) in binary?
Step 2: Apply Two’s Complement to 2010 (10100)2
How many bits do we need?
Rule of thumb: if left most bit is “1”, add an extra bit! (because negative numbers should always start with 1, and positive numbers should always start with a 0)
    (20)10 = (10100)2 🡪 (010100)2
Invert all the bits in step 1:
    010100 🡪 invert 🡪 101011
Add 1 to the inverted value
101011 + 1 = 101100
therefore, (-20)10 = (101100)2

## Slide 6: How do we calculate 4 + (-20) in binary?
Step 3: Add the two binary numbers
0 0 0 1 0 0 (use the same number of bits for both numbers!)
+ 1 0 1 1 0 0
-------------------------------
1 1 0 0 0 0

## Slide 7: How do we calculate 4 + (-20) in binary?
Step 4: Check your answer, convert back to decimal
1100002 is a negative number (begins with ‘1’) -- so first let’s apply the Two’s Complement rule to make it positive again.
Invert all the bits:
    110000 🡪 invert 🡪 001111
Add 1 to the inverted value 001111 + 1 = 010000
Convert to decimal
010000 = 24 = 16
This means we correctly calculated: 4 - 20 = -16 [end of solution]

## Slide 8: How do we calculate 4 + (-20) in binary?
Steps (Review)
Converting 4 and 20 to binary
Apply Two’s Complement rule to (-20)
  How many bits do we need to represent -20? Rule of thumb: since left most bit of 20 is a “1”, add an extra bit!
Add the two binary numbers
  Important: use all of the bits from step 2 for both numbers
Check your answer: convert the result to decimal
  Trick: if the answer is negative, apply Two’s Complement rule again before converting to decimal

## Slide 9: How to do these problems in general?
Steps (no matter what the numbers are)
Convert from decimal to binary
Apply Two’s Complement rule to all negative numbers
  Important: choosing the right number of bits to use. Rule of thumb: if left most bit is a 1, add an extra bit
Add the two binary numbers
  Important: use all of the bits from step 2
Check your answer: convert the result to decimal
  Trick: if the answer is negative, apply Two’s Complement rule again before converting to decimal

## Slide 10: Review: How many bits do we need to represent a number?
1 bit 🡪 can represent 2 unsigned numbers
    (unsigned: no distinction between positive and negative)
  (0)2 = (0)10
  (1)2 = (1)10
2 bits 🡪 can represent 4 unsigned numbers
  (00)2 = (0)10
  (01)2 = (1)10
  (10)2 = (2)10
  (11)2 = (3)10
  Values: 0 to 3 in decimal.

## Slide 11: Review: n Bits ⬄ How many Numbers
n bits
Can represent 2n numbers
Values: from 0 to (2n -1)
1 Byte 🡪 8 bit 🡪 28 numbers (256)
First Number 0000 00002 = (0)10 to
Last Number 1111 11112 = 28-1 = (255)10
Check your understanding -- please ask your classmates and/or MIO me if you don’t know the answers to these questions!
How many unsigned numbers can I represent in 4 bytes? What is the first and last number?

## Slide 12: Review: Two’s Complement: Representation with 4 bits
1 0 0 0 -8
1 0 0 1 -7
1 0 1 0 -6
1 0 1 1 -5
1 1 0 0 -4
1 1 0 1 -3
1 1 1 0 -2
1 1 1 1 -1
0 0 0 0 0
0 0 0 1 1
0 0 1 0 2
0 0 1 1 3
0 1 0 0 4
0 1 0 1 5
0 1 1 0 6
0 1 1 1 7
How many signed numbers can we represent with 4 bits in Two’s complement?
Still the same magnitude (4 bits -> 24 total numbers)
But: the values you can represent are approximately halved (because half of the numbers you’re representing are now negative!)
So instead of 0 -> 15 (unsigned)
We now have -8 -> 7 (signed)

## Slide 13: Exercises: To Complete in Class (hand in your progress by end of class)
Steps (show your work for each step!)
Convert from decimal to binary
Apply Two’s Complement rule to all negative numbers
Add the two binary numbers
Check your answer: convert the result to decimal
Questions 1. What is 22 - 3?
2. What is 32 - 8?
3. What is 14 - 17?
4. What is 6 - 30?