## Slide 1: Technical Support (420-1N6-AB) Binary Electronics & Logic Gates
Fall 2023

## Slide 2: Boolean Logic & Logic Gates

## Slide 3: Fundamentals of logic circuit
1946 ENIAC Computer – First programmable electronic (stands for Electronic Numerical Integrator and Computer)
The first programmers Betty Jean Jennings and Fran Bilas at the School of Electrical Engineering. During the war, these women developed an expertise and became hard to replace by the returning soldiers.

## Slide 4: Logic in Electronics
Processors work by reacting to an input of 0s and 1s in specific ways and then returning an output based on the decision.
The decision itself happens in a circuit called a logic gate, each of which requires at least one transistor, with the inputs and outputs arranged differently by different operations.

## Slide 5: The advent of transistors
Invented in 1947, transistors revolutionized the computing world.
They came to replace the vacuum tubes that were used back then as signal regulator.
This is a 2nm IBM wafer containing hundreds if chips which allows 50 billion transistors onto a chip of a fingernail

## Slide 6: Transistors count in computers
Number of transistors in an integrate circuit (IC) doubles every two years.
BUT! Since 2010, semiconductor advancement has slowed industry-wide.
Physical limits of transistors

## Slide 7: What is really a transistor
Miniature semiconductor element of a circuit that controls the voltage flow, amplifies it and can act as switch/gate.
Notes: A transistor is a switch made up of three connectors called the Base, Emitter and Collector and finally a semi-conductor.
A base electrode you can control the semi-conductor (just like a light switch)
You can switch the current millions of times per second.
More transistors allows us to create the Boolean operations (And, OR, XOR, NOT)
The use those logic gates can be used to make math operation (adder, multiplexer)

## Slide 8: Logic in Electronics
Electrical circuits are designed to represent logical expressions
  Known as logic circuits.
Used to make important logical decisions in household appliances, computers, communication devices, traffic signals and microprocessors.
Four basic logic operations listed below:
  OR operation
  AND operation
  NOT operation
  XOR operation (eXclusive Or)

## Slide 9: Boolean Operations
Integrated Circuits (microchips) are used to store and manipulate (process) bits.
Bits can be manipulated using Boolean Operations.
Boolean algebra: the mathematics of digital logic and Boolean operations.
  Name Boolean for mathematician George Boole
  Useful in dealing with binary systems where a variable can have a false of 0 or 1 (true or false).
  Uses Boolean operations to manipulate one or more Boolean values.
  Used in the analysis and synthesis of logical expressions.

## Slide 10: Logic Gates
A logic gate is an electronic circuit/device which makes the logical decisions based on these operations.
Logic gates have:
  One or more inputs
  Only one output
  Computes a Boolean operation.
The output is active only for certain input combinations.
Logic gates are the building blocks of any digital circuit.

## Slide 11: Logic Gate & Truth Tables
Using Truth Tables we can use different sets of logic operations to store, add, subtract, and perform more complicated operations with bits.

## Slide 12: Boolean Operations: AND
AND Operation
  Both input values must be TRUE for output to be TRUE
  Shrek is an ogre AND Fiona is a princess
  Both inputs are TRUE, so the output is TRUE
TRUE
TRUE
AND
=TRUE

## Slide 13: Boolean Operations: AND Gate
Truth Table
Inputs Outputs
0 0 0
0 1 0 0 = FALSE
1 0 0 1 = TRUE
1 1 1
AND Operation
Both input values must be TRUE for output to be TRUE
0
0
0
0
1
0
1
0
0
1
1
1

## Slide 14: AND Gate
To build an AND gate: Two transistors connected together
Two inputs (transistors A and B) and one output
Transistor A: Off (False)
Transistor B: On (True)
Output: Off (False)
Off (False)
On (True)
Off (False)

## Slide 15: AND Gate
Transistor A: On (True)
Transistor B: On (True)
Output: On (True)
On (True)
On (True)
On (True)

## Slide 16: Boolean Operations: OR
OR Operation
  Both input values must be FALSE for output to be FALSE
  If Michael likes traffic OR Michael takes the train to work every day ☹. 🡪 False or False = False
  Both inputs must be FALSE for an OR expression to be FALSE.
  If Michael is to change his habits and use public transit 🡪 expression becomes true. (One true is enough)
FALSE
FALSE
OR
= FALSE

## Slide 17: Boolean Operations: OR Gate
Truth Table
Inputs Outputs
0 0 0
0 1 1 0 = FALSE
1 0 1 1 = TRUE
1 1 1
OR Operation
At least one input value must be TRUE for output to be TRUE
0
0
0
0
1
1
1
0
1
1
1
1

## Slide 18: Logic Gates are circuits
Modern computers use transistors combined with resistors and diodes to build logic gates,
DIY Logic Gates: https://www.youtube.com/watch?v=sTu3LwpF6XI&t=481s&ab_channel=BenEater

## Slide 19: OR Gate
Two inputs (transistors A and B) and one output.
Transistor A: Off (False)
Transistor B: Off (False)
Output: Off (False)

## Slide 20: OR Gate
Two inputs (transistors A and B) and one output
Transistor A: Off (False)
Transistor B: On (True)
Output: On (True)

## Slide 21: Boolean Operations: NOT
Truth Table
Inputs Outputs
0 1 0 = FALSE
1 0 1 = TRUE
NOT Operation
Only one input
Opposite of input (inverts input)
NOT FALSE = TRUE
NOT TRUE = FALSE
0
1
1
0

## Slide 22: NOT Gate
To build an NOT gate: One transistor
One input and one output
Transistor A: On (True)
Current flows to ground wire and none to output, so output is Off (False)

## Slide 23: Boolean Operations: XOR
XOR Operation (Exclusive OR)
  One and ONLY one input value can be TRUE for output to be TRUE
  At noon Michael is going for lunch XOR Michael is going to class
  If both were true, the output would be false! (as I cannot do both at the same time).
  If both were false, the output will still be false
TRUE
FALSE
OR
=TRUE

## Slide 24: Boolean Operations: XOR Gate
Truth Table
Inputs Outputs
0 0 0
0 1 1 0 = FALSE
1 0 1 1 = TRUE
1 1 0
XOR Operation
Only one input value is TRUE for output to be TRUE
0
0
0
0
1
1
1
0
1
1
1
0

## Slide 25: NOT Gate
Transistor A: Off (False)
Current flows to the output wire, so output is On (True)

## Slide 26: XOR Gate
How to build an XOR gate? We can’t do it directly with transistors-- but we can by combining AND, OR, and NOT gates!
Both of the images above are the same combination of gates; the only difference is the input values

## Slide 27: Logic Gates and Binary Math

## Slide 28: Activity: Digit Addition
Design a logic circuit made up of one of the simple gates we have seen so far: AND, OR, XOR, NOT to perform an addition A + B:
A B | C S
0 0 | 0 0
0 1 | 1 0
1 0 | 1 0
1 1 | 0 1
Addition truth table

## Slide 29: Half Adder Gate: Adding two bits
Inputs: A, B
S = Sum
C = Carry
A + B = 2’s 1’s

## Slide 30: Half Adder Gate: Adding two bits
Inputs: A, B
S = Sum
C = Carry
A + B = 2’s 1’s
0 + 0 = 0 0
0 🡪
0 🡪
0
0

## Slide 31: Half Adder Gate: Adding two bits
Inputs: A, B
S = Sum
C = Carry
A + B = 2’s 1’s
0 + 1 = 0 1
0 🡪
1 🡪
1
0

## Slide 32: Half Adder Gate: Adding two bits
Inputs: A, B
S = Sum
C = Carry
A + B = 2’s 1’s
1 + 0 = 0 1
1 🡪
0 🡪
1
0

## Slide 33: Half Adder Gate: Adding two bits
Inputs: A, B
S = Sum
C = Carry
A + B = 2’s 1’s
1 + 1 = 1 0
1 🡪
1 🡪
0
1

## Slide 34: Full Adder
Why do we call it a half adder? Because if you are performing two additions in a row such as 1 + 1 +1
D

## Slide 35: Full Adder
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 |  | 
Homework….

## Slide 36: 8 bits Full adders

## Slide 37: Marble Adding Machine
http://www.youtube.com/watch?v=GcDshWmhF4A&NR=1&feature=fvwp

## Slide 38: Back to the CPU
The CPU ALU (Arithmetic logic unit) is made up of a combination of logic circuits paced at the clock signal. The ALU is able to perform those operations:
  Add
  Add with carry
  Subtract
  Subtract with borrow
  Two’s complement
  Increment
  Decrement
  Pass through
  Logical operations (and, or, xor, not or one’s complement)
  Bit shift operation

## Slide 39: This is a 4-bit CPU

## Slide 40: Why is the this important?
The logical circuits of the CPU determines the bus width of your system:
32-bit CPU
64-bit CPU
More on this in lecture 6...

## Slide 41: Questions?